## Slide 1: Energy Efficient Cooling
Saurabh Diddi
Director

## Slide 2: Bureau of Energy Efficiency
Energy Conservation (EC) Act 2001
Norms for Energy Intensive Industries
Standard & Labeling
Energy Conservation Building Code
Demand Side Management
Certification of Energy Professionals
BEE Established on
1st March 2002 under EC Act
Implement regulatory and promotional functions of EC Act.
Reduce Energy Intensity of our country
Has State Designated Agencies in each state for enforcement and awareness

## Slide 3: India’s Energy Profile
Chart: Energy Intensity - toe/GDP (1000 USD)
| 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0 | 2026.0 | 2027.0 | 2028.0 | 2029.0 | 2030.0
GDP Billion USD | 1123.37 | 1227.44 | 1333.1 | 1384.97 | 1502.42 | 1656.56 | 1766.53 | 1863.41 | 1985.28 | 2127.81 | 2296.63 | 2430.2984 | 2585.2069 | 2746.2616 | 2913.4625 | 3086.8096 | 3266.3029 | 3451.9424 | 3643.7281 | 3841.66 | 4045.7381 | 4255.9624 | 4472.3329 | 4694.8496 | 4923.5125 | 5158.3216
TPES Mtoe | 516.16 | 543.28 | 573.98 | 602.21 | 663.21 | 693.22 | 722.64 | 758.37 | 776.37 | 826.19 | 851.13 | 884.8864 | 916.3814 | 947.4276 | 978.025 | 1008.1736 | 1037.8734 | 1067.1244 | 1095.9266 | 1124.28 | 1152.1846 | 1179.6404 | 1206.6474 | 1233.2056 | 1259.315 | 1284.9756
Energy Intensity toe/GDP (1000 USD) | 0.45947 | 0.44261 | 0.43056 | 0.43482 | 0.44143 | 0.41847 | 0.40907 | 0.40698 | 0.39106 | 0.38828 | 0.3706 | 0.36411 | 0.35447 | 0.34499 | 0.33569 | 0.32661 | 0.31775 | 0.30914 | 0.30077 | 0.29265 | 0.28479 | 0.27717 | 0.2698 | 0.26267 | 0.25578 | 0.24911

## Slide 4: Per Capita Energy Consumption
Chart: Per Capita Energy Consumption
| 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0 | 2026.0 | 2027.0 | 2028.0 | 2029.0 | 2030.0
TPES/Population toe/capita | 0.45106 | 0.4675 | 0.48655 | 0.50307 | 0.54622 | 0.56314 | 0.57929 | 0.60017 | 0.60678 | 0.63784 | 0.6492 | 0.66559 | 0.68075 | 0.69521 | 0.709 | 0.72214 | 0.73465 | 0.74655 | 0.75787 | 0.76862 | 0.77883 | 0.78851 | 0.79768 | 0.80636 | 0.81456 | 0.8223

## Slide 5: Growth in Building Sector
Chart: 
Residential Elec (Mtoe) | 9.13 | 10.16 | 10.68 | 11.38 | 12.5 | 13.73 | 15.2 | 16.19 | 17.6 | 19.09 | 21.24
Chart: 
Commercial Elec (Mtoe) | 3.61 | 4.07 | 4.3 | 4.8 | 5.37 | 5.87 | 6.1 | 6.65 | 6.8 | 7.14 | 8

## Slide 6: Growth in Building Sector
Chart: Building Sector Growth
| 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0 | 2026.0 | 2027.0 | 2028.0 | 2029.0 | 2030.0
Residential Mtoe | 9.13 | 10.16 | 10.68 | 11.38 | 12.5 | 13.73 | 15.2 | 16.19 | 17.6 | 19.09 | 21.24 | 22.8497 | 24.7933 | 26.8551 | 29.0351 | 31.3333 | 33.7497 | 36.2843 | 38.9371 | 41.7081 | 44.5973 | 47.6047 | 50.7303 | 53.9741 | 57.3361 | 60.8163
Commercial Mtoe | 3.61 | 4.07 | 4.3 | 4.8 | 5.37 | 5.87 | 6.1 | 6.65 | 6.8 | 7.14 | 8 | 8.205 | 8.6191 | 9.0324 | 9.4449 | 9.8566 | 10.2675 | 10.6776 | 11.0869 | 11.4954 | 11.9031 | 12.31 | 12.7161 | 13.1214 | 13.5259 | 13.9296

## Slide 7: Cooling Profile - India
Chart: Electricity Consumption – 1200 BU
| Domestic | Commercial | Industry | Agriculture | Public Lighting | Traction | Public Works | Misc
 | 0.26586 | 0.098788 | 0.34888 | 0.20275 | 0.011371 | 0.020694 | 0.02548 | 0.026172
Air Conditioner Contribution:
Household: 20-30%
Commercial: 40-50%
70-80 GW connected load is only due to Cooling and consumes about 40-50 BU annually
Notes: Surviving Stock: 25.67 million units of Room AC
Eq TR is 34.65 million TR (Average of Country is 1.35 TR per Room AC)
Average EER is 3.1
Hence 39.18 GW connected load due to Room Air Conditioner
RAC is 50% of total cooling Market, Hence 70-80 GW connected load due to cooling in India in 2014
Annual electricity consumption is based on 1200 hours of operation and 50% working out of total connected load, hence about 48 BU with 80GW connected load

## Slide 8: Cooling Market
Chart: Segment Share of Air Conditioning
| Room Air Conditioner | Central Plant (Chiller) | Duct/Package | VRF | Precision
 | 50 | 24 | 14 | 6 | 6
Chart: Room Air Conditioner Market
| Commercial | Residential
 | 40 | 60

## Slide 9: Urban Households Possessing Appliances per 1000 households
Approx. 6% in Urban Household
Notes: 214 AC & cooler per 1000 urban household, with assumption of 30% AC and 70% cooler in urban household. This ratio will be 64/1000 household which is about 6.4% penetration

## Slide 10: 2030 Scenario
Challenge
Opportunity
Conservative Scenario
Aggressive Scenario

## Slide 11: Opportunities & Challenges
Opportunity
  Higher Penetration
  Sales growth
  More cooling requirement due to climate change & rise in incomes
  Efficient Air Conditioners
Challenges
  Significant peak load contribution due to cooling requirements
  High Electricity consumption
  High cost of Efficient Air Conditioners
  Inefficient air conditioners installed
  Maintenance & Power Supply issues

## Slide 12: Room Air Conditioners
Mandatory Appliance
Standard: IS 1391:1992
Section 14(b): S.O.180(E) dated 12.01.2009
Section 14 (a): S.O. 181 (E) dated 12.01.2009
Regulation: No.2 /11(5)/03-BEE dated 06.07.2009
Star Labeling Parameter
Energy Efficiency Ratio
Window AC
Split AC
Higher is Better

## Slide 13: Inverter Air Conditioners
Voluntary Appliance
Standard: ISO 16358
Performance factor: Indian Seasonal Energy Efficiency Ratio (Higher is better)

## Slide 14: ISEER Methodology
ISEER – Indian Seasonal Energy Efficiency Ratio
Testing standard – IS 1391 Part II
Calculation procedure – ISO 16358
Weather profile for 54 cities across India were analysed to arrive bin temperature and hours
Bin Hours- 1600
Bin temperature - 24 – 43 °C.

## Slide 15: How Inverter AC Works?

## Slide 16: How Inverter ACs have more Energy saving potential?

## Slide 17: Fixed Speed AC

## Slide 18: Fixed Speed AC

## Slide 19: ISEER Methodology

## Slide 20: ISEER Calculations

## Slide 21: Comparison – Variable and Fixed speed AC

## Slide 22: Star level up-gradation for Split AC (2006-11 to 2018-19)

## Slide 23: Change in Label
Jan 2018

## Slide 24: Market Transformation
Chart: 2016-17
| Star 1 | Star 2 | Star 3 | Star 4 | Star 5
 | 20 | 310323 | 4334168 | 105953 | 1679444
Chart: 2018 (As it is)
| Star 1 | Star 2 | Star 3 | Star 4 | Star 5
 | 3776934 | 35935 | 2161278 | 70018 | 75400
ISEER: 3.3

## Slide 25: Market Transformation
Chart: 2016-17
| Star 1 | Star 2 | Star 3 | Star 4 | Star 5
 | 20 | 310323 | 4334168 | 105953 | 1679444
Chart: 2018
| Star 1 | Star 2 | Star 3 | Star 4 | Star 5
 | 3776934 | 35935 | 2161278 | 70018 | 75400
Chart: 2018 (Proposed)
| Star 1 | Star 2 | Star 3 | Star 4 | Star 5
 | 20 | 310323 | 4334168 | 105953 | 1679444
ISEER: 3.9 - 4.0
Efficiency Improvement: 18-21%

## Slide 26: Market Transformation
Chart: 
| 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2017.0 | 2018.0
Year | 2.61 | 2.66 | 2.72 | 2.79 | 2.83 | 2.95 | 2.98 | 3.17 | 3.26 | 3.3 | 3.9

## Slide 27: Key Items to look into for NCAP
Demand Reduction
  Building Energy Efficiency
    Commercial Building – Thermal Comfort & Appliance Efficiency
    Residential Building – Thermal Comfort
  Appliances
    More reliability
    Efficient Installation
Affordability
Efficient Appliances
District Cooling

## Slide 28: Thank You for Your Kind Attention