## Slide 1
EESL’s Initiative in National Cooling Action Plan
17 January, 2018

## Slide 2: EESL Super Efficient Air Conditioning Programme (ESEAP)
Bulk Procurement Mechanism

## Slide 3: The Imperative- ACs contribute to peak demand
Studies show that the additional demand from room ACs in India is equivalent to 200-300 large (500 MW) power plants by 2030 i.e. 100-150 GW and 10% of energy demand (~ 300 TWh)
This implies
  Significant addition to the grid generation capacity (read Coal based)
  OR
  Investing in in-situ diesel generators or battery inverters
  Eventually increasing consumer tariffs
One AC
2 Ceiling Fans
2 Incandescent Bulbs
4 Tube lights
One TV
One Refrigerator
Source: Lawrence Berkeley National Lab (LBNL), USA

## Slide 4: The Case for Market Side Intervention
Policy led rating programme has improved energy efficiency with time
Urbanization led rising AC demand (CAGR ~ 15%)
Yet
Slow inverter technology push (only 20% till date; major markets >75%)
Negligible low GWP options (HCFCs like R-290 / R-32/ R-410A/ blends)

## Slide 5: The ESEAP Product

## Slide 6: Customers Want
  Product
    First Costs & Running Costs
    Warranty
    After Sales experience
  Easy Financing options
Super Efficiency (ISEER 5.2, 1.5 ton)
  Split configuration Inverter technology
    33% efficient from 5 Star
  Low GWP
Assurance
  Comprehensive warranty – 3 year; Compressor (5 years)
  Tested to work in conditions like 52°C, Pollution
Convenience
  Installation and 3 year annual service by brand
  Buyback option
  Financing options
ESEAP Offering

## Slide 7: Impact: Aggregation of AC market
  100,000 ACs, rated ISEER 5.2 AC1 at rational prices2 with
  3 year all comprehensive warranty
  ACs supplied via institutional channels (and not retail)
  Co-benefits
    Higher uptake of Low GWP refrigerants (R-410A, R-290)
    Design for India (works even at 52°C, polluted regions)
1: 33% more efficient than the 5-Star rated AC with EER of 3.5
2: nearly 30% discount to expected open market prices
EESLs market led approach to
deliver cooling for India,
without heating up the planet

## Slide 8: Cost Analysis
Source: EESL calculations,
ESEAP AC analysed against 5 star AC- 2014, 2015, (expected) 2018
Payback time based on expected consumer savings against incremental spend on 5 star product
All inclusive price includes installation , warranty and annual service
Conclusion
Drop the idea of purchasing a 5 star rated AC today;
Simply purchase EESL super efficient AC.
 | 3 Star Inverter AC | 5 Star Inverter AC | Super Efficient Inverter AC
ISEER | 3.2 | 4.2 | 5.2
Electricity Wattage | 1650 | 1250 | 1015
Market price | 40,000 | 45,000 | 54,500
5 year AMC | 20,000 | 20,000 | 3000
Annual operating days | 225 | 225 | 225
Operating Hours per day | 10 | 10 | 10
Annual Electricity Consumption Units | 3000 | 2275 | 1850
Annual Electricity Charges @ 8 Rs. | 24000 | 18200 | 14800
Electricity Charges for 5 years | 1,20,000 | 91,000 | 74,000
Total Cost for 5 years | 180K | 156K | 131K

## Slide 9
Thank You