## Slide 1
Indian Polyurethane Association 17 Jan 2018 New Delhi
National Cooling Action Plan Seminar

## Slide 2
Polyol
Fire retardant (Optional)
Surface active agent
Accelerating agent
Water
Blowing agent
Isocyanates
Isocyanates
Isocyanates
Polyurethane
Polyols
Mixed
Polyurethane Foam

## Slide 3
India Insulation Forum (IIF)
India Insulation Forum (IIF ) was created as a sub unit under IPUA
to promote INSULATION in the building envelop/Cold Chain
industry to enhance and promote Energy Efficiency.
IIF is represented by reputed companies and processors who make different
materials for Insulation used for energy efficiency in buildings and Cold Storages.
IIF is heterogenous group , but is,
Technology NEUTRAL
Product NEUTRAL
Company NEUTRAL
Promotes the concept of Energy Efficiency

## Slide 4
Spray Foam Alliance of India ( SFAI )
A sub-unit of IPUA created to address two important issues.
First – to bring into effect the simplest and most effective form of INSULATION –
Spray Polyurethane Foam
Second – to train the crucial link in the industry chain – the APPLICATOR
alongwith machinery manufacturers
INSULATION is a game changing factor in the Energy Efficiency program
Technical
Manual
A Guide to
Energy
Security
WORKING WITH SPRAY POLYURETHANE FOAM

## Slide 5
Spray Foam Alliance of India( SFAI )
Insulation Material | Thermal Conductivity Coefficient
Spray Polyurethane Foam | 0,023 W/mK
Expanded Polystyrene EPS | 0,030 - 0,047 W/m K
Extruded Polystyrene XPS | 0,029 - 0,037 W/m K
Mineral Wool | 0,033 - 0,044 W/m K
A comparison of Thermal Conductivity Co-efficient shows Spray Foam
the leader.

## Slide 6
  Stops heat / cold ingress from outside
  Saves on fossil fuel
  Reduces emission of GHG.
  Lower energy losses; avoid the danger of oversized heating or cooling systems that works hard to compensate for the heat or cold losses through the building envelope.
Environmental
  Effective insulation lowers heating or cooling bills, thus no longer being affected by rising energy costs
  Maintains controlled temperature for longer periods.
  Reduces wastage of perishables like Fruits and vegetables
Economical
  Human Comfort – improves the efficiency of occupier or user.
  Provides fungus-free and microbe-free healthier environment
Social
Insulation Benefits

## Slide 7
Efficient Insulation Products
Fibrous/Mineral Wool Materials
Rock wool
Glass Wool
Slag Wool
Rigid Insulation Materials
Expanded Polystyrene ( EPS )
Extruded Polystyrene (XPS )
Polyurethane Foam ( PU )
Polyisocyanurate Foam ( PIR )

## Slide 8
Roof Insulation ( Over Deck & Under Deck )
Over deck Insulation:
PU Spray Insulation on roof
Over deck Insulation XPS on Roof
Under deck Insulation:
XPS
Over deck Insulation: XPS & PUF slabs

## Slide 9
Dry Wall Insulation with Mineral Wool
PU Spray Insulation- Interior Walls & Roof
External Wall Insulation with XPS
Curtain Wall Insulation XPS (External Walls)
Wall Insulation – Internal & External

## Slide 10
Different Application Methods
Basement Insulation
Floor Insulation
Direct to Deck Metal Roof
Cavity Wall Insulation- XPS
Inverted Roof Concept
Spray Foam

## Slide 11
PU External Thermal Insulation Composite System
PU Roof Insulation with
water proofing membrane
Different Application Methods - Polyurethane

## Slide 12
Five Climate Zones in India
ECBC refers to these and suggest different compliance for different zones
Hot – Dry
Warm – Humid
Composite
Temperate
Cold
R value Specified for all zones (roofs & walls)
Climate Map of India
Source : ECBC

## Slide 13: ECBC Requirements: Prescriptive (Roof)
Maximum U-factor is prescribed for the complete roof assembly.
Minimum R-value is prescribed for insulation alone (excluding air films)
Recommendations made for proper placement, installation and protection of insulation
Source : ECBC

## Slide 14
ECBC Requirements: Prescriptive ( Wall )
Maximum U-factor is prescribed for the complete wall assembly
Minimum R-value is prescribed for insulation alone (excluding air films)
Source : ECBC

## Slide 15
Heat Load Components - Warm Humid Climate - Chennai
Summer Heat Flow (May) | 
Weather Conditions | 
Temperature | Min.: 18.7oC, Max.: 42.6oC, Avg.: ~32oC
Relative Humidity | Min.: 13%, Max.: 97%, Avg.: ~50%
Net heat flow per unit area | 
Roof (15 m2) | 17.0 kWh/m2
Wall (47.6 m2) | 7.3 kWh/m2
Window (8.4 m2) | 44.5 kWh/m2
Infiltration (based on floor area 15 m2) | 4.9 kWh/m2
Roof: 25%
Wall: 32%
Windows: 36%
Infiltration: 7%
Source : BEEP

## Slide 16
Roof: 31%
Wall: 32%
Windows: 31%
Infiltration: 6%
*Direct heat gain from windows not accounted
Source : BEEP
Summer Heat Flow (May) | 
Weather Conditions | 
Temperature | Min.: 18.7oC, Max.: 42.6oC, Avg.: ~32oC
Relative Humidity | Min.: 13%, Max.: 97%, Avg.: ~50%
Summer Heat Flow (May) | 
Weather Conditions | 
Temperature | Min.: 18.7oC, Max.: 42.6oC, Avg.: ~32oC
Relative Humidity | Min.: 13%, Max.: 97%, Avg.: ~50%
Heat Load Component – Composite Climate ( Delhi )

## Slide 17
School building in a typical summer day in Composite climate (Indore, M.P.)
With a roof of 40mm insulation with metal cladding
  Up to 6-7oC cooler than ambient
  Up to 4-5oC cooler than RCC
Impact of Roof Insulation
Source : BEEP

## Slide 19
Challenges
Awareness
Mandatory
Implementation issues
Energy Guzzling Buildings
Life Cycle Analysis
Standardization

## Slide 20
Indian Polyurethane Association in its own way tries to promote
Energy Efficiency through its sub-groups of IIF & SFAI.
IPUA conducts Training programs at different locations to
keep the industry abreast of the needs
IPUA conducts Seminars on Insulation with specialists
in the field of Energy Efficiency
IPUA conducts training programs on Insulation in Polytechnics
Conclusion

## Slide 21
Thank You