## Slide 1: Introduction of Alternative Refrigerant in the Thailand AC Sector
Annual 2017 Network Meeting of the National Ozone Officers
Of the South Asia Countries
23 – 26 May 2017
Agra, Uttar Pradesh, India
Viraj Vithoontien
Lead Environmental Specialist
The World Bank Group

## Slide 2: Thailand AC Sector Case Study and Intellectual Property Rights (IPR)
Thailand’s air-conditioning (AC) sector in context
Challenges in converting to non-HCFC tech.
  Technology and the market
  IPR and technology transfer
  Standards and safety
  Component availability
Brokering solutions that work for all
Thailand’s experience: A springboard to improved energy efficiency and additional climate co-benefits
Outline
IPR
Intellectual property protection: background and relevance
IPR in relation to future Montreal Protocol (MP) implementation
IPR and technology transfer
Notes: This morning we heard a couple of case studies in adoption of R-32 technology – I will continue in this vein, with the specific experience of Thailand in adopting an HCFC alternative technology in residential AC manufacturing with some discussion on intellectual property rights and technology transfer
I will start with some contextual information on Thailand and AC, and then move to the challenges encountered in the conversions – first in terms of the alternative technologies available and market circumstances, then on IPR, because it figured so prominently in the negotiations on the HFC amendment and will continue to be a major issue as we move forward, I will go over some basics and also findings of a World Bank study on IPR.
Back to the Thailand case, I will summarize the lessons learned and how these have set the stage for pursuing additional co-benefits through adoption of alternative and advanced technologies.

## Slide 3: Thailand’s AC Sector in Context
2nd largest residential AC manufacturing base in E. Asia and major export hub: ~ 10 million units/yr (10% for local market) made of multinationals + 14 Thai companies.
Market somewhat segmented with local companies focused on the domestic and lower-end markets, as well as larger units.
At project baseline (2012):
  Sector dominated by HCFC-22 based manufacturing (95% of AC sold are R-22 units), growth at 7%
  To meet obligations to the Montreal Protocol on Substances that Deplete the Ozone Layer of 10% reductions from the baseline, Thailand needed to eliminate 8,800 tons of HCFCs under BAU.
  43% of Thailand’s HCFC consumption went towards refrigeration and AC manufacturing.
  Critical to address AC sector to slow R-22 demand in manufacturing and downstream servicing.
  AC sector has the technology to convert if necessary: R410A (already the technology of choice in developed countries; components and markets assured).
Project funding considerations – refrigerant technology has to be lower in GWP…
Notes: Timeline: April 2012 HPMP submitted. R-410 A chosen – multinationals already producing/able to go to 410A, local companies felt pressure to go to this tech. Plus components were readily available.
July 2012 –Resubmitted with same technology but no go. WB realized that the project would not be approved so long 410A was the choice. At that point started the consultation and review process for selecting another technology.
ExCom was concerned if the whole sector went to R-410A as the market was v. large with global implications
Had a valid concern

## Slide 4: Challenges: Technology and the Market
Alternative refrigerant technology other than R-410A is new – not tested nor used in developed countries.
First decision by potential beneficiaries (Thai-owned enterprises): Which refrigerant technology?
Considerations: R-290 vs. R-32
  R-290 - Highly flammable, already stigmatized by a high profile accident in Thailand despite voluntary handling standard; high costs in safety measures and training (aftersales)
  R-32 - Mildly flammable; major manufacturer is developing and testing the technology, moderate costs in safety measures but aftersales training costs also high
Concerns centered primarily on safety and standards, technology access, market acceptability and competitors, and size of typical AC manufactured.
Industry prefers R-32 after weighing pros/cons and benefits/risks of the two.
Notes: Barriers to conversion
International standard exists to build on –its on refrigerants but nothing for A2L. ISO 5149 revised in 2014.
Size of AC mattered due to refrigerant charge.

## Slide 5: Challenges: Technology and the Market
R-32 becomes the candidate refrigerant – but not all enterprises are convinced that: + a grant is a better option than no grant + R-410A because of fears:
  Market acceptability (flammability, costs)
  Availability of technology
  Use of / applying the technology in face of capacity and policy constraints
Market acceptability is to be tackled on several fronts: Create confidence and scale through involvement of a major player while assuring small enterprises they will not be shut out of the market, and may gain – together this can overcome the R-410A bias.
  Dialogue with Daikin leads to agreement that it launches R-32 in the market but timing tbd.
  Dialogue with Thai industry leads to 6 interested companies (out of 14) that accept some markets (EU) will close if they go to R-410A and are open to learn more about R-32…
Availability of the technology …R-32 technology is patented by Daikin.
Another dynamic at play – other multinationals in Thailand were not willing to pay for R-32 and prepared to undermine the technology’s credibility in Thailand.
Notes: Here explain that other multinationals that did not have R-32 were already campaigning against flammable, unsafe r-32 AC.

## Slide 6: Challenges: IPR and Technology Transfer
In the case of residential air-conditioning, Daikin had already agreed to provide developing countries free access to 93 basic application patents as a means to encourage commercialization for HFC-32 based AC.
Thai industry is still reluctant – that does not give it know-how. Although technology choice has been made and is accessible thru an agreement with Daikin, there is still the “doing” left which requires intensive efforts and guidance.
  WBG-Daikin organize a factory visit in Japan for the industry on equipment installation and safety measures
  Multiple consultations organized with the 14 companies, within the association (Thai AC Club) and bilaterally
A deal on applying the technology is reached:
  Daikin agrees to also provide tailored support to participating companies to improve AC quality (“clean-dry-tight” manufacturing approach) during project implementation
  The return is more reliable, quality R-32 AC market to build confidence in the product and demand as this is new, high-profile – high risk for market acceptability - Daikin stands to benefit, with direct access to the Thai market
Remaining issues:
  Thai industry requires one last assurance – when will Daikin market R-32 AC in Thailand. Agreement on 2015 is reached after consultations and meetings in DC, Thailand and Japan. One more tour, enterprise balance join.
  Opposition by other multinational AC manufacturers in Thailand: METI puts pressure on the companies to accept R-32 technology as this aligns with Japanese domestic policy on high GWP gases; Policy needed.
Notes: Type of agreement reached/signed with Daikin: non-assertion agreement
Non-assertion of intellectual property rights – provision in a license agreement that terminates the license if the license brings an infringement suit against the licensor or certain of the licensor’s products, commonly those falling within terms of license. This is particularly common in licenses granted by patent pools because licensor members of the pool would otherwise lose ability to use the licensed patents defensively, i.e. in normal circumstances the licensor would have used the patents to secure a cross-license from an industry participant. (“yank clause”)
So contracting party will not assert patents or other IP rights against the other contracting party, even if that party were to engage in an infringing use.
They permit the contracting parties to avoid costly litigation over the use of an IP righ. Kind of like non-exclusive, royalty free licenses
***these types of agreements can facilitate exchange of information, provision of details that otherwise might be used by the liencense to develop a blocking patent position. They are procompetitive because both parties avid hidden blocking patents

## Slide 7: Challenges: Standards and Safety
Restrictions on the use of flammable refrigerant in AC in high-rise buildings – would this apply to R-32? Regulatory agencies needed clarity….
  Thailand Council of Engineers, based on request from Department of Industrial Works (DIW), confirms that HFC-32 is not considered a highly flammable substance.
  DIW commissions an independent safety assessment of HFC-32 in split-type AC equipment. Conclusion: HFC-32 can be safely used in a split-type with cooling capacity not over 53,500 Btu/hr (15.75kW) provided the inside unit is wall-mounted.
  WBG reviews ISO-5149-2014 which recommends a max. refrigerant charge size for A2L (mildly flammable) and A3 (highly flammable) refrigerants based on building occupancy category and equipment location. Slide deck is prepared for discussion on revising building code.
  WBG shares experiences of other countries on dealing with HFC-32 refrigerant – primarily Japan’s research: risk assessment studies on HFC-32 carried out by the Japan Refrigeration and Air-Conditioning Industry Association (JRAIA).
Based on tests and evidence, Department of Public Works and Town Country Planning decides to modify regulation to allow installation of split-type AC with capacity up to 36,000 Btu/hr in high-rises. For larger units, consultation is underway.
Who benefits? Thai domestic industry and multinationals.
About 6 months
Notes: 36,000 BTU limit is set for the worst case scenario which is when the equipment is installed on the floor. If a/c is installed on the wall or on the ceiling, the study found it is safe up to 50000 BTU per hour.

## Slide 8: Challenges: Component Availability and Supply
Design of refrigerant pathway required a new compressor
One rotary compressor manufacturer supplying the market for all types of refrigerant compressors in the most popular size range. But for larger TR units (about 10% of the market and belonging to the Thai industry) there was a gap.
Critical mass and coordinated efforts were needed to convince supplier to produce the R-32 compressor in larger size range – but this was not evident to private sector players who tend to go it alone (competition)

## Slide 9: Brokering Solutions that Work for All
Identification and isolation of the challenge or hurdle
Systematically addressing the challenge (step by step) while consulting stakeholders all along
Building consensus among stakeholders by singling out the bottom line/interest of each
Fostering confidence of policy-makers in new technology through information, particularly that from developed countries
Technology Choice
Technology Transfer and Knowhow
Enablers: Policy, Standards & Codes, Grants
Supply of Components
Market Acceptance
Market Penetration
2015: R-32 based AC introduced in Thailand by multinationals.
2016: 3 Thai AC manufacturers introduce R-32 AC; 30,000 units sold.
January 1, 2017 ban of >50,000 Btu R-22 AC manufacturing for domestic market.
Performance of R-32 AC is better than similar R-22 & R-410 units.
AC Club of the Federation of Thai Industries is a stronger collective, better able to meet evolving market demands as a unified front.
Lessons on the importance of guaranteeing compressor supply led to a Canadian grant to assist a Thailand reciprocating compressor manufacturer to design and develop R-32 based compressors.
Results
Notes: Important to note that project is not completed – there are still things to do such as build lab capacity to safely test R-32 prototypes for certification and to build capacity of technicians and building operators to handle R-32 refrigerants and equipment.
Performance is better as they are tighter, more leak proof – R-32 is more efficient
8 more enterprises will finish this year. All will produce R-32 units – 90% of their production in 2017

## Slide 10: Building from Thailand’s Experience
Positive experience (new markets, more sales) of Thai AC manufacturers is their motivation to take the next big step - move from fixed speed to inverter technology (also for light commercial AC). Initiatives to support this move are under consideration by Government of Thailand and the WB.
Thailand’s technology transfer and technical assistance program will serve as a model for other countries with AC companies that want to convert from HCFC-based manufacturing (Vietnam) or improve manufacturing quality(Jordan).
Treatment of A2L refrigerant for use in residential AC in building codes can be replicated in other countries.
Spin-off R-32 reciprocating compressor activity (EFO) has laid the foundation for alternative compressor technology in commercial refrigeration and AC, the latter which is essential in high-ambient, harsh conditions. Testing the compressor in the low-GWP refrigerant AC demo in S. Arabia is being explored.
India request to the WBG for a $200 million loan for transitioning to superefficient AC – the conversion experiences of Thailand re. refrigerant technologies to be incorporated, and potentially benefitting from an established working relationship with multinational AC industry.
Notes: Essentially – lessons learned
Both Daikin and Mitsubishi have already introduced R-32 inverter tech. in Thailand