## Slide 1
Overview of Challenges in the Network for Introduction of ODS alternative Technologies in Foam Sector
INDIAN POLYURETHANE ASSOCIATION ( IPUA )
Presentation by:
Samir Arora
24th May, 2017 - Agra

## Slide 2
Polyol
Fire retardant (Optional)
Surface active agent
Accelerating agent
Water
Blowing agent
Isocyanates
Isocyanates
Polyurethane
Polyols
Mixed
Polyols

## Slide 3
India - HCFC Phase Out
Chart: 
| Commercial Refigration | Tharmoware | Discontinuous Panels | General Insulation & Spray | Integral Skin | Water Heaters | Continuous Panels & Sheets
Phase II Enterprises (440 Nos) | 120 | 95 | 90 | 75 | 32 | 25 | 3
PHASE - II
Discontinues
Panels
Water Heater
Thermoware
Commercial Refrigeration
General Insulation
Integral Skin
Cyclopentane Methyl Formate HFCs HFOs Methylal
Ecomate
Continuous Panel & Sheets

## Slide 4
Transitioning from HCFC 141b
Domestic Refrigeration
Article V Countries
HCFC 141 b
Cyclopentane
HCFC 141 B
Methyl Formate/ Ecomate
245fa and Blends (water, pentane, 365mfc, others
HFOs & Blends

## Slide 5
Innovating to Enable Industry growth
Transitioning from HCFC 141b
Domestic Refrigeration
Performance Cost-effective Environment
Safety
Long term solution already
Available. For energy may need improvement which can lead to use of blends of CP and HFOs
Current: Transition to:
Assessment Future Impact
Article V Countries
Environment friendly blowing
agent, can easily replace
HCFC 141 b. dynamically priced which can be adopted easily by SMEs.
Cyclopentane
HCFC 141 B
Methyl Formate/ Ecomate
Performance Cost-effective Environment
Safety

## Slide 6
Innovating to Enable Industry growth
Transitioning from HCFC 141b
PHASE - I
Domestic Refrigeration
Current: Transition to:
Assessment Future Impact
Medium term solution, can
meet energy standards, may
need transition to 4th
generation BA future to meet
GWP standards
Energy efficient blowing
agent with very low GWP.
In the best position
for future
Article V Countries
245fa and Blends (water, pentane, 365mfc, others
HFOs & Blends
Performance Cost-effective Environment
Safety
Performance Cost-effective Environment
Safety
HCFC 141 B

## Slide 7
Innovating to Enable Industry growth
Cyclopentane – a proven solution
PHASE - I
Domestic Refrigeration
Universally accepted for rigid foams productions for Medium and Large Industries
In use for many years in refrigerating appliances
Good availability as it is a by product of refineries
lower molecular weight thus less required
No toxicity related issues
Though highly flammable can be handled safely with properly designed equipment
Polyol and C5 blend does not posses high fire risk
Initial capital cost is high but running cost is low , as it is the lowest cost BA

## Slide 8
Innovating to Enable Industry growth
Challenges
PHASE - I
Domestic Refrigeration
Various blowing agents are in offering as alternative- making selection confusing
New technologies are not fully adoptable because of high capital cost
Phase-II stakeholders will be competing against large units using Cyclopentane technology
Not easy for them to adopt Cyclopentane technology due to lack of fund or infrastructure, Whereas cyclopentane is Fire Hazardous.
Due to high capital cost and Fire hazardous properties it is challenging for micro & small enterprises to adopt to cyclopentane technology.

## Slide 9
In the world market for more than a decade. Proven in wide range of applications since 2002, including refrigeration, marine, automotive, construction , sandwich panels, spray foam and many more
A very good thermal efficient Blowing agent
Can replace HCFCs, HFCs, HCs & HFOs Environmentally Benign and Economically advantageous
Regulator compliant - US EPA, SNAP, MONTREAL AND KYOTO Protocol
Properties similar to 141-b with half the molecular weight, hence less quantities for same density. Hence cost effective
Ease of change over with minimal capital expenses. Means very ideal for change over for SMEs. Can be processed through standard and/existing equipments
ECOMATE is stored and shipped in metal containers.
Excellent miscibility with all major Polyols and compatible with most PU raw materials
No need to emulsify blowing agent
Blended POLYOL does not possess any fire risk
Available worldwide
– a proven solution

## Slide 10
- Challenges
Apprehensions
Corrosive? NO. It is stored and transported in MS Drums. It is just an apprehension.
Shrinkage: Expert guidance & Proper formulation is required to eliminate any such possibility
Seal Compatability: Change of SEAL is a MUST. EPDM is acceptable. For Polyol /Resin PU systems with ~5% ecomate®, PTFE, Kalrez, EPDM, Butyl, Viton, Neoprene and silicone have proven acceptable.
Pure form is flammable: Yes, but in blended form it is 100% safe and transported normally.

## Slide 11
Innovating to Enable Industry growth
HFOs
PHASE - I
Domestic Refrigeration
This is another alternate tried and tested but have two main challenges
Foam Sector is not aware of the price
Availability of HFOs still not known

## Slide 12
Innovating to Enable Industry growth
Water
PHASE - I
Domestic Refrigeration
This is another alternate tried and tested but have two main challenges
It does not work in low density foam manufacturing
Does not have good insulation properties thus has limitation in many sectors

## Slide 13
Overall Challenges – Medium Sector
To adopt the new Technology
The larger the selection of Blowing Agents – more the confusion
Unfortunately newer Technologies are not being adopted because of awarness
Medium sectors have challenges vis-a-vis Enterprises who have already adopted the Pentane technology
Pentane technology is not easily adoptable due to lack of Funds and infrastructure coupled with huge capital cost, fire safety issues etc. The Pentane technology operating cost are reportedly low.
Even HFOs will be out of reach of many Enterprises due to cost and availability.
This segment should be prioritized first.
There is no one alternate that fits all segments

## Slide 14
Overall Challenges -Small Scale Sector
Majority of them are not aware that there is a BA which needs replacement
This is because they buy pre-blended Polyol and suppliers do not disclose
Low consumption of BA limits -adapting to Pentanes/HFOs
High prices of HFO results in high cost of the final product.
Pre-blended pentane is safe & successful –however miscibility with polyol is an issue
Suppliers of Systems have to guide small scale sector correctly

## Slide 15
Large Sector : This sector will have a fairly smoother transition to go to HCFC free alternate as the technology is well adapted now.
Although safety still remains challenge even for this sector.
Conclusion - Large Sector

## Slide 16
This sector will face challenges as to which technology they will need to adopt. To overcome these challenges , they will need to be supported with :-
  Regular awareness program.
  System Houses from whom they buy System will need to support them in HCFC free technology.
  SMEs from each sector need to visit other manufacturing units where HCFC free Technology is being used.
  Demonstration of using new HCFC Free technology is a must
  Suppliers of HCFC free alternates need to provide free consultation.
Conclusion - SME Sector

## Slide 17
THANK YOU FOR YOUR ATTENTION